## Slide 1: An Introduction to Routing the Internet
Geoff Huston
APNIC

## Slide 3
2 85.132.40.1 (85.132.40.1) 1.202 ms 1.272 ms 1.425 ms
3 94.20.50.141 (94.20.50.141) 2.394 ms 2.649 ms 2.044 ms
4 r02-greenxchange-r04.az-ix.net (85.132.60.61) 2.634 ms 2.700 ms 2.292 ms
5 so-7-0-0-ycr1.skt.cw.net (166.63.220.21) 71.707 ms 77.259 ms 78.499 ms
6 xe-0-3-1-xcr2.amd.cw.net (195.2.9.217) 102.346 ms
xe-0-2-1-xcr2.amd.cw.net (195.2.9.233) 103.459 ms
xe-0-3-1-xcr2.amd.cw.net (195.2.9.217) 100.372 ms
7 ae3-xcr1.amd.cw.net (195.2.30.105) 98.816 ms 99.660 ms 97.998 ms
8 xe-4-1-0-xcr1.lsw.cw.net (195.2.25.93) 97.892 ms
xe-7-2-0-xcr2.lsw.cw.net (195.2.25.138) 97.840 ms
xe-4-1-0-xcr1.lsw.cw.net (195.2.25.93) 132.251 ms
9 xe-3-0-1-xcr1.lns.cw.net (195.2.25.250) 101.963 ms 97.870 ms 97.707 ms
10 195.66.236.166 (195.66.236.166) 102.975 ms 101.481 ms 107.319 ms
11 i-2-0-0.ulco-core01.bi.telstraglobal.net (202.40.148.218) 104.572 ms 98.277 ms 102.415 ms
12 i-6-0-0.eig-core01.bx.telstraglobal.net (202.84.249.21) 241.369 ms 238.537 ms 240.648 ms
13 i-0-4-1-0.eqnx-core01.bi.telstraglobal.net (202.84.249.34) 239.569 ms 239.580 ms 239.513 ms
14 i-0-4-0-0.sydo-core02.bx.telstraglobal.net (202.84.144.186) 386.366 ms 386.084 ms 398.815 ms
15 tengige0-2-0-0.oxf-gw1.sydney.telstra.net (203.50.13.29) 388.800 ms 399.029 ms 397.750 ms
16 bundle-ether1.ken-core4.sydney.telstra.net (203.50.6.5) 394.591 ms 406.403 ms 396.072 ms
17 bundle-ether5.cha-core4.brisbane.telstra.net (203.50.11.73) 410.061 ms 411.584 ms 413.307 ms
18 tengigabitethernet7-1.cha30.brisbane.telstra.net (203.50.51.40) 432.973 ms 401.504 ms 400.854 ms
19 4608resolvers.brisbane.telstra.net (139.130.130.194) 405.478 ms 407.010 ms 408.246 ms
20 wattle.rand.apnic.net (203.133.248.2) 406.757 ms 410.261 ms 410.676 ms

## Slide 4: The Objective of Routing
To ensure that every packet gets delivered
  To ensure that every packet gets delivered in the shortest possible time
This implies that every router needs to understand the relative direction of all possible destinations
So every router needs to know the current relative location of all possible destinations
This is the task of the routing system

## Slide 5: Routing Architecture
The Internet uses a decoupled routing architecture
  A routing protocol is designed to pass forwarding information between routers. It does not perform the forwarding function itself
  Different networks may (and do) use different routing protocols
  Routing protocols change over time
    But need not change all at once

## Slide 6: Routing Protocols
Routing protocols are “self discovery” distributed protocols
  Two flavours of algorithm:
    Distance vector (rumours)
      I tell you everything I know
      You tell me everything you know
      Repeat until nothing more to day!
    Link State (map drawing)
      I tell everyone about my links (link state messages)
      I listen to all link state messages
      I compute a optimal path map of the network

## Slide 7: Routing Architecture
The Internet uses a two level routing hierarchy:
  Interior Routing Protocols, used by each network to determine how to reach all destinations that line within the network
  Interior Routing protocols maintain the current topology of the network

## Slide 8: Routing Architecture
The Internet uses a two level routing hierarchy:
  Exterior Routing Protocol, used to link each component network together into a single whole
  Exterior protocols assume that each network is fully interconnected internally

## Slide 9: Exterior Routing: BGP
BGP is a large set of bilateral (1:1) routing sessions
  A tells B all the destinations (prefixes) that A is capable of reaching
  B tells A all the destinations that B is capable of reaching
A
B
10.0.0.0/24
10.1.0.0/16
10.2.0.0/18
192.2.200.0/24

## Slide 10: BGP decisions
BGP is an “offer and accept” protocol
  A network “offers” to a neighboring network prefixes that it is prepared to act as a forwarder
  The network need not offer all its prefixes to a routing neighbour
    It may have internal routing policies to moderate what it is prepared to offer
  The neighboring network is not obliged to accept the offer
    It may have better offers from other routing peers that show a preferred path
    It may have policies about redistribution of prefixes that determine what is offered and what is accepted

## Slide 11: A view of a Routing Table
show ip bgp
BGP table version is 0, local router ID is 203.133.248.2
Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,
r RIB-failure, S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
Network Next Hop Metric LocPrf Weight Path
* 1.0.0.0/24 202.12.28.1 0 4777 15169 i
*> 203.119.76.3 0 4608 15169 i
* 1.0.4.0/22 202.12.28.1 0 4777 2516 6453 7545 7545 7545 56203 i
*> 203.119.76.3 0 4608 1221 2764 24130 7545 7545 56203 i
*> 1.0.16.0/23 202.12.28.1 0 4777 2519 i
* 203.119.76.3 0 4608 1221 4637 3356 2516 2519 i
*> 1.0.18.0/23 202.12.28.1 0 4777 2519 i
* 203.119.76.3 0 4608 1221 4637 3356 2516 2519 i
*> 1.0.20.0/23 202.12.28.1 0 4777 2519 i
* 203.119.76.3 0 4608 1221 4637 3356 2516 2519 i
*> 1.0.22.0/23 202.12.28.1 0 4777 2519 i
* 203.119.76.3 0 4608 1221 4637 3356 2516 2519 i
*> 1.0.24.0/23 202.12.28.1 0 4777 2519 i
* 203.119.76.3 0 4608 1221 4637 3356 2516 2519 i
*> 1.0.26.0/23 202.12.28.1 0 4777 2519 i

## Slide 12: Routing Properties
Routing is designed to be robust
  Within a richly connected topology the interior routing protocol is designed to “self heal” in the even of breakage
  Within the exterior network, connectivity will also “self heal” if there are alternative paths that route around the break
Routing is efficient
  Interior routing can be tuned to converge in milliseconds
  Exterior routing will converge across the span of the Internet within 70 seconds on average following a change in local connectivity

## Slide 13: Routing Policies
Exterior routing systems are often used to express a number of objectives:
  Business requirements (e.g.: customer, peer, upstream)
  Traffic Engineering requirements (e.g.: traffic flow balancing)
  Robustness requirements (e.g.: alternate connection arrangements and automated failover)

## Slide 14: Routing Insights
Routing is essentially a view of “all of the network” at once, and as such it provides a number of useful insights into the connected network

## Slide 15: The Big Picture of the v4 Routing Table
Introduction of
CIDR – March 1994
The Great Internet Boom
and Bust of 2000/2001
Broadband to the Masses
The GFC hits the Internet
Address Exhaustion

## Slide 16: Routing Issues

## Slide 17: The Big Picture of the v4 Routing Table
Introduction of
CIDR – March 1994
The Great Internet Boom
and Bust of 2000/2001
Broadband to the Masses
The GFC hits the Internet
Address Exhaustion

## Slide 18: Hot topics in Routing
Security

## Slide 19: Hot Topics in Routing
2004
100,000
500,000
2008
2012
2016
300,000
Scaling

## Slide 20: Open Routing Standards
Interior Routing Protocols
  Open Shortest Path First (OSPF)
  Intermediate System – Intermediate System (IS-IS)
Exterior Routing Protocols
  Border Gateway Protocol (BGP)