## Slide 1: The 512K route thing

## Slide 2: 12 August 2014
Newborn Panda Triplets in China
Rosetta closes in on comet 67P/Churyumov-Gerasimenko
World Elephant Day

## Slide 3
The Internet apparently has a bad hair day

## Slide 4: What happened?
Did we all sneeze at once and cause the routing system to fail?

## Slide 5: Well someone sneezed!

## Slide 6: 12 August 2014
Verizon Route Leak (AS701)

## Slide 7: But route leaks happen all the time
But not from AS701!
  AS701 is a tier 1 ISP
  So very few (noone?) filters what they hear from AS701
  Which means that when AS701 leaks all non-default AS’s (and a few more besides) are likely to hear the route leak
So everybody saw a bunch of routes for a small amount of time…

## Slide 8: Minute by Minute ANNces & WDLs

## Slide 9: Minute by Minute ANNces & WDLs

## Slide 10: Second by Second

## Slide 11: Second by Second
07:49.15 Table exceeds 512K
07:49:45 First set of withdrawals
07:49:58 Second set of announcements
07:50:20 Third set of announcements
07:52:04 Fourth set of announcements
07:52:46 Second wave of Withdrawals start
07:58:20: All done

## Slide 12
http://www.cisco.com/c/en/us/support/docs/switches/catalyst-6500-series-switches/116132-problem-catalyst6500-00.html
http://www.brocade.com/downloads/documents/html_product_manuals/NI_05600_ADMIN/wwhelp/wwhimpl/common/html/wwhelp.htm#context=Admin_Guide&file=CAM_part.11.2.html
Cisco Cat 6500
Brocade NetIron XMR
512K is a default constant
in some of the older Cisco
and Brocade products

## Slide 13: What happens then?
Crash and reboot?
Crash and die?
Push excess routes to slow path?
Discard excess routes
Was there any evidence of dropped routes?

## Slide 14: Dropped Routes?
Net change of -450 routes

## Slide 15: Maybe there’s more…

## Slide 16: Collateral Damage
Outside of AS701, a further ~2,000 routes were withdrawn between 07:47 and 12:00, but some of these were probably part of the route leak as they appeared to be part of the Verizon enterprise structure. But there were others who were clearly unrelated to Verizon…

## Slide 17: Collateral Damage
763 Origin ASes were probably affected
AS Pfxs AS Name
9658 391 ETPI-IDS-AS-AP Eastern Telecoms Phils., Inc.,PH
6648 127 BAYAN-TELECOMMUNICATIONS Bayan Telecommunications, Inc.,PH
23498 75 CDSI - COGECODATA,CA
21332 60 NTC-AS OJSC "Vimpelcom",RU
27882 59 Telefonica Celular de Bolivia S.A.,BO
30036 56 MEDIACOM-ENTERPRISE-BUSINESS - Mediacom Communications Corp,US
131222 51 MTS-INDIA-IN 334,Udyog Vihar,IN
6459 45 TRANSBEAM - I-2000, Inc.,US
46805 42 CACHED - CachedNet LLC,US
45664 42 LBNI Liberty Broadcasting Network Inc,PH
8402 40 CORBINA-AS OJSC "Vimpelcom",RU
55465 38 TTT-AS-AP TT&T Co,TH
18025 38 ACE-1-WIFI-AS-AP Ace-1 Wifi Network,PH
22363 36 PHMGMT-AS1 - Powerhouse Management, Inc.,US
15085 33 IMMEDION - Immedion, LLC,US
50710 32 EARTHLINK-AS EarthLink Ltd. Communications&Internet Services,IQ
27229 32 WEBHOST-ASN1 - Webhosting.Net, Inc.,US
21284 32 VIVODI-AS ON S.A.,GR
23606 31 BELLTELECOM-PH-AS-PH Bell Telecommunication Philippines,PH
7018 30 ATT-INTERNET4 - AT&T Services, Inc.,US
50576 30 KRASNET-UA-AS Krasnet ltd.,UA
16058 30 Gabon-Telecom,GA
13188 30 BANKINFORM-AS TOV "Bank-Inform",UA

## Slide 18: But then it happened again!
BGP FIB Size
A second time!
Verizon Leak!

## Slide 19: So maybe we should broaden the question…
Was the AS701 Route Leak the problem?
Or was the FIB growth passing 512K entries the problem?

## Slide 20: There is no Routing God!
There is no single objective “out of the system” view of the Internet’s Routing environment.
BGP distributes a routing view that is modified as it is distributed, so every eBGP speaker will see a slightly different set of prefixes, and each view is relative to a given location
When we look at some of the route collector sites we see a variance of ~20,000 routes across the routing peer set

## Slide 21: The RouteViews View
2010
now
300,000
500,000

## Slide 22: Zooming in
12 August
512K
10 October

## Slide 23: For most networks…
(probably including yours)
Its likely that your router’s routing table has yet to pass over the 512K point
  (Except for the occasional route leak of course)
So there is still some time to check if you can cope with a steady-state default free routing table with more than 512K entries

## Slide 24: For most networks…
For most affected networks, it was the AS701 route leak that tipped them over the edge on the day
However, passing through 512K routes in the IPv4 routing table is inevitable
When? And what’s next?
How quickly is the routing table growing?

## Slide 25
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Broadband to the Masses
2009: The GFC hits the Internet
2011: Address Exhaustion
20 years of routing the Internet

## Slide 26: IPv4 BGP Prefix Count 2011 - 2014
Jan
2011
Jan
2012
350,000
450,000
550,000
Jan
2013
Jan
2014
Jan
2015

## Slide 27: IPv4 in 2014 – Growth is Slowing (slightly)
Overall IPv4 Internet growth in terms of BGP is at a rate of some ~9%-10% p.a.
Address span growing far more slowly than the table size (although the LACNIC runout in May caused a visible blip in the address rate)
The rate of growth of the IPv4 Internet is slowing down (slightly)
  Address shortages?
  Masking by NAT deployments?
  Saturation of critical market sectors?

## Slide 28: IPv6 BGP Prefix Count
2,000
10,000
20,000
Jan
2011
Jan
2012
Jan
2013
Jan
2014
0
World IPv6 Day

## Slide 29: IPv6 in 2013
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2012 growth rate was ~ 90%.
If these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in ~16 years time

## Slide 30: What to expect

## Slide 31: BGP Size Projections
For IPv4 this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
  which makes this projection even more
  speculative than normal!

## Slide 32: V4 - Daily Growth Rates

## Slide 33: V4 - Relative Daily Growth Rates

## Slide 34: V4 - Relative Daily Growth Rates

## Slide 35: IPv4 BGP Table Size predictions
Jan 2013 441,172 entries
2014 488,011 entries
2015 540,000 entries 559,000
2016 590,000 entries 630,000
2017 640,000 entries 710,000
2018 690,000 entries 801,000
2019 740,000 entries 902,000
These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.
Linear Model
Exponential Model

## Slide 36: IPv6 Table Size
2004
2010
0
15,000
20,000
2008
2012
2014
10,000
25,000
5,000
2006

## Slide 37: V6 - Daily Growth Rates

## Slide 38: V6 - Relative Growth Rates

## Slide 39: V6 - Relative Growth Rates

## Slide 40: V6 - Relative Growth Rates

## Slide 41: IPv6 BGP Table Size predictions
Jan 2013 11,600 entries
2014 16,200 entries
2015 24,600 entries 19,000
2016 36,400 entries 23,000
2017 54,000 entries 27,000
2018 80,000 entries 30,000
2019 119,000 entries 35,000
Exponential Model
LinearModel

## Slide 42
Moore’s Law
BGP Table Size Predictions
IPv4 BGP Table size and Moore’s Law

## Slide 43: IPv6 Projections and Moore’s Law
Moore’s Law
BGP Table Size Predictions

## Slide 44: BGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing rapidly, is still relatively small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm it will continue to be viable for some time yet

## Slide 45: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 46: Announcements and Withdrawals

## Slide 47: Convergence Performance

## Slide 48: IPv4 Average AS Path Length
Data from Route Views

## Slide 49: Updates in IPv4 BGP
Nothing in these figures is cause for any great level of concern …
  The number of updates per instability event has been constant, due to the damping effect of the MRAI interval, and the relatively constant AS Path length over this interval
What about IPv6?

## Slide 50: V6 Announcements and Withdrawals

## Slide 51: V6 Convergence Performance

## Slide 52: V6 Average AS Path Length
Data from Route Views

## Slide 53: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
But whether this is a problem or not depends on the way in which routers handle the routing table.
So lets take a quick look at routers…

## Slide 54: Inside a router
Backplane
Line Interface Card
Switch Fabric Card
Management Card
Thanks to Greg Hankins

## Slide 55: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 56: Inside a line card
CPU
PHY
Network
Packet Manager
DRAM
TCAM
*DRAM
Media
Backplane
FIB Lookup Bank
Packet Buffer
Thanks to Greg Hankins

## Slide 57: FIB Lookup Memory
The interface card’s network processor passes the packet’s destination address to the FIB module.
The FIB module returns with an outbound interface index

## Slide 58: FIB Lookup
This can be achieved by:
  Loading the entire routing table into a Ternary Content Addressable Memory bank (TCAM)
or
  Using an ASIC implementation of a TRIE representation of the routing table with DRAM memory to hold the routing table
Either way, this needs fast memory

## Slide 59: TCAM Memory
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
192.0.0.0/16 11000000 00000000 xxxxxxxx xxxxxxxx 3/0
192.0.2.0/24 11000000 00000000 00000010 xxxxxxxx 3/1
11000000 00000000 00000010 00000001
Longest Match
The entire FIB is loaded into TCAM. Every destination address is passed through the TCAM, and within one TCAM cycle the TCAM returns the interface index of the longest match. Each TCAM bank needs to be large enough to hold the entire FIB. TTCAM cycle time needs to be fast enough to support the max packet rate of the line card.
TCAM width depends on the chip set in use. One popular TCAM config is 72 bits wide. IPv4 addresses consume a single 72 bit slot, IPv6 consumes two 72 bit slots. If instead you use TCAM with a slot width of 32 bits then IPv6 entries consume 4 times the equivalent slot count of IPv4 entries.

## Slide 60: TRIE Lookup
Address
Outbound Interface identifier
192.0.2.1
I/F 3/1
11000000 00000000 00000010 00000001
1/0
1/0
1/0
1/0
1/0
x/0000
?
?
?
?
?
…
?
The entire FIB is converted into a serial decision tree. The size of decision tree depends on the distribution of prefix values in the FIB. The performance of the TRIE depends on the algorithm used in the ASIC and the number of serial decisions used to reach a decision
ASIC
DRAM

## Slide 61: Memory Tradeoffs
TCAM
Lower
Higher
Higher
Higher
Larger
80Mbit
ASIC +
RLDRAM 3
Higher
Lower
Lower
Lower
Smaller
1Gbit
Thanks to Greg Hankins
Access Speed
$ per bit
Power
Density
Physical Size
Capacity

## Slide 62: Memory Tradeoffs
TCAMs are higher cost, but operate with a fixed search latency and a fixed add/delete time. TCAMs scale linearly with the size of the FIB
ASICs implement a TRIE in memory. The cost is lower, but the search and add/delete times are variable. The performance of the lookup depends on the chosen algorithm. The memory efficiency of the TRIE depends on the prefix distribution and the particular algorithm used to manage the data structure

## Slide 63: Size
What memory size do we need for 10 years of FIB growth from today?
TCAM
V4: 2M entries (1Gt)
plus
V6: 1M entries (2Gt)
2014
2019
2024
512K
25K
125K
1M
768K
512K
V6 FIB
V4 FIB
Trie
V4: 100Mbit memory (500Mt)
plus
V6: 200Mbit memory (1Gt)
“The Impact of Address Allocation and Routing on the Structure and
Implementation of Routing Tables”, Narayn, Govindan & Varghese, SIGCOMM ‘03

## Slide 64: Scaling the FIB
BGP table growth is slow enough that we can continue to use simple FIB lookup in linecards without straining the state of the art in memory capacity
However, if it all turns horrible, there are alternatives to using a complete FIB in memory, which are at the moment variously robust and variously viable:
  FIB compression
  MPLS
  Locator/ID Separation (LISP)
  OpenFlow/Software Defined Networking (SDN)

## Slide 65: But it’s not just size
It’s speed as well.
10Mb Ethernet had a 64 byte min packet size, plus preamble plus inter-packet spacing
=14,880 pps
=1 packet every 67usec
We’ve increased speed of circuits, but left the Ethernet framing and packet size limits largely unaltered. What does this imply for router memory?

## Slide 66: Wireline Speed – Ethernet
1980
1990
2000
2010
2020
1Tb
10Mb
100Mb
1Gb
10Gb
100Gb
10Mb 1982/15Kpps
100Mb 1995 / 150Kpps
1Gb 1999 / 1.5Mpps
10Gb 2002 / 15Mpps
40Gb/100Gb 2010 / 150Mpps
400Gb/1Tb 2017?
1.5Gpps

## Slide 67: Clock Speed – Processors
1980
1990
2000
2010
2020
100Ghz
1Mhz
10Mhz
100Mhz
1GHz
10GHz
8080 2Mhz 1981
Dec Alpha 100Mz 1992
AMD 1GHz 2000
P4 3Ghz 2002
zEC12 5.5Ghz 2012

## Slide 68: Clock Speed – Processors

## Slide 69: CPU vs Memory Speed

## Slide 70: Speed, Speed, Speed
What memory speeds are necessary to sustain a maximal packet rate?
100GE 150Mpps 6.7ns per packet
400Ge 600Mpps 1.6ns per packet
1Te 1.5Gpps 0.67ns per packet
0ns
10ns
20ns
30ns
40ns
50ns
100Ge
400Ge
1Te

## Slide 71: Speed, Speed, Speed
What memory speeds do we have today?
0ns
10ns
20ns
30ns
40ns
50ns
Commodity DRAM
DDR3DRAM= 9ns -15ns
RLDRAM = 1.9ns - 12ns
Thanks to Greg Hankins
100Ge = 6.7ns
400Ge =1.67ns
1Te = 0.67ns

## Slide 72: Scaling Speed
Scaling size is not a dramatic problem today
Scaling speed is going to be tougher over time
Moore’s Law talks about the number of gates per circuit, but not circuit clocking speeds
Speed and capacity could be the major design challenge for network equipment in the coming years
If we can’t route the max packet rate for a terrabit wire then:
If we want to exploit parallelism as an alternative to wireline speed for terrabit networks, then is the use of best path routing protocols, coupled with destination-based hop-based forwarding going to scale?
Or are we going to need to look at path-pinned routing architectures to provide stable flow-level parallelism within the network to limit aggregate flow volumes?
Or should we reduce the max packet rate by moving away from a 64byte min packet size?
http://www.startupinnovation.org/research/moores-law/

## Slide 73
Thank You
Questions?