## Slide 1: Tyre Kicking the DNS Testing Transport Considerations of Rolling Roots
Geoff Huston
APNIC

## Slide 2: Five Years Ago

## Slide 3: The US KSK Repository

## Slide 4: The Amsterdam KSK Repository
George Michaelson

## Slide 5: Five Years Ago…

## Slide 6: Five Years Ago…

## Slide 7: Easy, Right?
Publish a new KSK and include it in DNSKEY responses
Use the new KSK to sign the ZSK (as well as the old KSK signature)
Withdraw the old signature signed via the old KSK
Revoke the old KSK

## Slide 8: Easy, Right?
Publish a new KSK and include it in DNSKEY responses
Use the new KSK to sign the ZSK (as well as the old KSK signature)
Withdraw the old signature signed via the old KSK
Revoke the old KSK
RFC 5011!

## Slide 9: Easy, Right?

## Slide 10: Easy, Right?
. / IN / DNSKEY response size
1024 bit ZSK
2048 bit ZSK

## Slide 11: We’ve (sort of) done it before

## Slide 12: But that was then…
And this is now:
  Resolvers are now not so aggressive in searching for alternate validation paths when validation fails
      (as long as resolvers keep their code up to date, which everyone does – right?)
  And now we all support RFC5011 key roll processes
  And everyone can cope with large DNS responses
  So all this will go without a hitch
  Nobody will even notice the KSK roll at the root
  Truly ruly!

## Slide 13: But that was then…
And this is now:
  Resolvers are now not so aggressive in searching for alternate validation paths when validation fails
      (as long as resolvers keep their code up to date, which everyone does – right?)
  And now we all support RFC5011 key roll processes
  And everyone can cope with large DNS responses
  So all this will go without a hitch
  Nobody will even notice the KSK roll at the root
  Truly ruly!
Not!

## Slide 14: What we all should be concerned about…
That resolvers who validate DNS responses will fail to pick up the new DNS root key automatically
  i.e. they do not have code that follows RFC5011 procedures for the introduction of a new KSK
The resolvers will be unable to receive the larger DNS responses that will occur during the dual signature phase of the rollover

## Slide 15: What can be tested …
That resolvers who validate DNS responses will fail to pick up the new DNS root key automatically
  i.e. they do not have code that follows RFC5011 procedures for the introduction of a new KSK
Will resolvers be able to receive the larger DNS responses that will occur during the dual signature phase of the rollover

## Slide 16: So we’ve been testing
We are interested in sending DNSSEC-aware DNS resolvers a response that is much the same size as that being contemplated in a KSK key roll
And seeing whether they got the response

## Slide 17: Some Interesting Sizes
8 octets UDP pseudo header size
20 octets IPv4 packet header
40 octets maximum size of IPv4 options in an IPv4 IP packet header
40 octets IPv6 packet header
512 octets the maximum DNS payload size that must be supported by DNS
560 octets the maximum IPv4 packet size that must be supported by IPv4 DNS UDP systems
576 octets the largest IP packet size (including headers) that must be supported by IPv4 systems
913 octets the size of the current root priming response with DNSSEC signature
1,232 octets the largest DNS payload size of an unfragmentable IPv6 DNS UDP packet
1,280 octets the smallest unfragmented IPv6 packet that must be supported by all IPv6 systems
1,425 octets the largest size of a ./IN/DNSKEY response with a 2048 bit ZSK
1,452 octets the largest DNS payload size of an unfragmented Ethernet IPv6 DNS UDP packet
1,472 octets the largest DNS payload size of an unfragmented Ethernet IPv4 DNS UDP packet
1,500 octets the largest IP packet supported on IEEE 802.3 Ethernet networks

## Slide 18: EDNS(0) UDP Buffer sizes

## Slide 19: EDNS(0) UDP Buffer sizes

## Slide 20: EDNS(0) UDP Buffer sizes
Around the 1425 octet response size we will see
UDP response truncation rates of around 5.5%

## Slide 21: The Test Method
We are using a mechanism to measure the Internet from the “edge”:
  We use an ad with an active script element
  When a browser receives an impression of the ad the script is activated
  The script fetches a small number (5) of 1x1 blots, and then fetches a final blot to tell us which ones it actually received
  As long as every DNS name in the URLs of these blots is unique, then DNS and Web proxies can’t interfere!
  Our servers see the DNS queries and the Web fetches
  We can infer client-side behaviours based on these observations
* Acknowledgement and thanks to Google for supporting this work

## Slide 22: The Test
We are interested in resolvers who are DNSSEC aware (queries that contain the EDNS0 option with DNSSEC OK flag set on)
We would like to test larger responses:
  1,440 octets of DNS payload
We would like to test a couple of crypto protocols
  RSA
  ECDSA

## Slide 23: Testing
We are interested in those resolvers that are retrieving DNSSEC signature data, so we are looking for queries that include EDNS0 and DNSSEC OK flag set
How many resolver queries have DNSSEC OK set?

## Slide 24: EDNS(0) DNSSEC OK Set
76,456,053 queries
63,352,607 queries with EDNS(0) and DNSSEC OK set
= 83% of queries
777,371 resolvers
649,304 resolvers with EDNS(0) and DNSSEC OK set
= 84% of resolvers

## Slide 25: Large Responses
How well are 1,440 octet DNS responses handled when compared to much smaller responses?

## Slide 26: 1,440 octet RSA-signed Responses
9,113,215 tests
7,769,221 retrieved the 1x1 blot (85%)
2,644,351 queried for the DS record
849,340 queried for the DS record (but no blot fetch)
494,581 timed out (but no blot fetch)
72 appeared to fail the DNS

## Slide 27: 1,440 octet RSA-signed Responses
9,113,215 tests
7,769,221 retrieved the 1x1 blot
2,644,351 queried for the DS record
849,340 queried for the DS record (but no blot)
494,581 timed out (but no blot)
72 appeared to fail the DNS
Some 5% of experiments did not run through to completion.
For an online ad, this is not an unexpected outcome

## Slide 28: 1,440 octet RSA-signed Responses
9,113,215 tests
7,769,221 retrieved the 1x1 blot
2,644,351 queried for the DS record
849,340 queried for the DS record (but no blot)
494,581 timed out (but no blot)
72 appeared to fail the DNS
This is measuring USERS not RESOLVERS. Users
often use local configurations of 2 or more resolvers, and problems in one resolver appear to be fixed by the other resolver(s).

## Slide 29: Small vs Large
What happens when the response size grows above 1,472 octets?
1,440 Octets Payload
Experiments: 6,542,993
Web Fetch: 5,880,921
DS Fetch: 181,610
Timeout: 480,415
DNS Fail: 47
1,770 Octets Payload
Experiments: 6,566,645
Web Fetch: 5,992,617
DS Fetch: 167,119
Timeout: 401,831
DNS Fail: 5,078

## Slide 30: ECDSA vs RSA
The spec says that when a resolver encounters a zone signed only with algorithms that are not supported by the resolver then it will treat the zone as unsigned and not proceed with validation
Most resolvers determine the zone’s signing algorithms from the DS record
What happens when we compare a 1,440 octet response signed by RSA and a 1,440 octet response signed by ECDSA?

## Slide 31: 1,440 octet ECDSA-signed Responses
9,137,436 tests
7,766,572 retrieved the 1x1 blot
2,644,564 queried for the DS record
860,163 queried for the DS record (but no blot)
505,045 timed out (but no blot!)
5,656 appeared to fail the DNS

## Slide 32: 1,440 octet ECDSA-signed Responses
9,137,436 tests
7,766,572 retrieved the 1x1 blot
2,644,564 queried for the DS record
860,163 queried for the DS record (but no blot)
505,045 timed out (but no blot!)
5,656 appeared to fail the DNS
This is larger than RSA failure rates, but is still a small proportion of users affected. Some resolvers appear to have problems when presented with an unknown crypto protocol.

## Slide 33: IPv4 vs IPv6
Do resolvers prefer IPv4 over IPv6?
  Total Queries: 47,826,735
  Queries over V6: 394,816
  Number of Resolvers: 109,725
  Number of Resolvers
  using IPv6 for queries: 2,849

## Slide 34: IPv4 vs IPv6
Do resolvers prefer IPv4 over IPv6?
  Total Queries: 47,826,735
  Queries over V6: 394,816
  Number of Resolvers: 109,725
  Number of Resolvers
  using IPv6 for queries: 2,849
In a Dual Stack environment 1% of queries and 3% of resolvers use IPv6.
What if the server was IPv6 only?

## Slide 35: Some Observations
There is a LOT of DNSSEC validation out there
  87% of all queries have DNSSEC-OK set
  30% of all DNSSEC-OK resolvers attempt to validate the response
  25% of end users are using DNS resolvers that will validate what they are told
  12% of end users don’t believe bad validation news and turn to other non-validating resolvers when validation fails.

## Slide 36: Some Observations
There is very little V6 being used out there
  1% of queries use IPv6 as the transport protocol when given a dual stack name server
It seems that when given a choice:
  Browsers prefer IPv6
  Resolvers prefer IPv4

## Slide 37: Some Observations
ECDSA is viable – sort of
  1 in 5 clients who use resolvers that validate RSA-signed responses are unable to validate the same response when signed using ECDSA
  But they fail to “unsigned” rather than “invalid” so it’s a (sort of) safe fail

## Slide 38: Can it work?
If we stick to RSA and keep response sizes at or below 1,440 octets then there appears to be no obvious user impact in terms of packet size
  Some resolvers may get stuck, but users appear to use multiple resolvers

## Slide 39: Questions?
Geoff Huston
George Michaelson