## Slide 1: DNS Privacy (or not!)
Geoff Huston
APNIC

## Slide 2
https://xkcd.com/1361/

## Slide 3: Why?
Because everything you do on the net starts with a call to the DNS
If we could see your stream of queries in real time we could assemble a detailed profile of you and interests and activities
Do we have any evidence of DNS data mining?
  Data miners don’t disclose their sources as a rule

## Slide 4: Why?
Because everything you do on the net starts with a call to the DNS
If we could see your stream of queries in real time we could assemble a detailed profile of you and interests and activities
Do we have any evidence of DNS data mining?
  Data miners don’t disclose their sources as a rule
How about something related:
  Do we have any evidence of DNS stalking?

## Slide 5: What if…
I gave you an absolutely unique name to resolve:
  The name never existed before now
  The name will never be used again
  The name includes the time when the name was created
If I am the authoritative server for the name’s zone then I should see your efforts to resolve the name
Then I should never see the name as a resolution query ever again
  Unless you have attracted a digital stalker who performs re-queries of your DNS names!

## Slide 7: DNS Re-query Rate
Over the past 30 days, some 5.3% of users have some kind of DNS stalker that is asking the same query more than 30 seconds after the initial query
Only some of these could be explained by incredibly slow DNS resolver systems
Daily Counts
Daily Ratios

## Slide 8: DNS Stalking
There are two kinds of DNS stalkers
  Rapid tracking stalkers that appear to track users in real time
  Bulk replay stalkers that replay DNS queries at a very high rate in bursts

## Slide 9: DNS Stalking Age
DNS Stalking uses both really recent data and more than year-old data!

## Slide 10: DNS Surveillance
The DNS appears to be used by many actors as a means of looking at what we do online and censoring what services we can access online

## Slide 11: DNS Surveillance
The DNS appears to be used by many actors as a means of looking at what we do online and censoring what services we can access online
Can we stop DNS surveillance completely?
  Probably not!
Can we make it harder to collect individual profiles of activity?
  Well, yes
  And that’s what I want to talk about today

## Slide 12: The DNS Privacy Issue
Lots of actors get to see what I do in the DNS
  My platform
  My ISP’s recursive resolver
  Their forwarding resolver, if they have one
  Authoritative Name servers
  Snoopers on the wire
Can we make it harder for these “others” to snoop on me?

## Slide 13: How we might think the DNS works
Client
DNS Resolver
DNS Server

## Slide 14: What we suspect the DNS is like
Client
DNS Resolver
DNS Server
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver

## Slide 15: What we suspect the DNS is like
Client
DNS Resolver
DNS Server
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
DNS Resolver
Corrupted host platforms
Wireline and middleware
Inspection and interception
Resolvers that leak queries
Servers that leak queries

## Slide 16: Why pick on the DNS?
The DNS is very easy to tap
  Its open and unencrypted
DNS traffic is easy to tamper with
  Its payload is not secured and tampering cannot be detected
  Its predictable and false answers can be readily inserted
The DNS is hard to trace
  Noone knows exactly where their queries go
  Noone can know precisely where their answers come from

## Slide 17: Second-hand DNS queries are a business opportunity these days

## Slide 18: How can we improve DNS Privacy?
Lets look at a few behaviours of the DNS and see what we are doing to try and improve its privacy properties

## Slide 19: The DNS is overly chatty
The DNS uses the full query name to discover the identity of the name servers for the query name
  Hi root server, I want to resolve www.example.com
  Not me – try asking the servers for .com

## Slide 20: The DNS is overly chatty
The DNS uses the full query name to discover the identity of the name servers for the query name
  Hi root server, I want to resolve www.example.com
  Not me – try asking the servers for .com
  Hi .com server, I want to resolve www.example.com
  Not me – try asking the servers for example.com

## Slide 21: The DNS is overly chatty
The DNS uses the full query name to discover the identity of the name servers for the query name
  Hi root server, I want to resolve www.example.com
  Not me – try asking the servers for .com
  Hi .com server, I want to resolve www.example.com
  Not me – try asking the servers for example.com
  Hi example.com server, I want to resolve www.example.com
  Sure – its 93.184.216.34

## Slide 22: The DNS is overly chatty
The DNS uses the full query name to discover the identity of the name servers for the query name
  Why are we telling root servers all our DNS secrets?
  In our example case, both a root server and a .com server now know that I am attempting to resolve the name www.example.com
  Maybe I don’t want them to know this

## Slide 23: The DNS is overly chatty
Is there an alternative approach to name server discovery that strips the query name in iterative search for a zone’s servers?
  Yes – the extra information was inserted into the query to make the protocol simpler and slightly more efficient in some cases
  But we can alter query behaviour to only expose as much as is necessary to the folk who need to know in order to answer the query

## Slide 24: QNAME Minimisation
A resolver technique intended to improve DNS privacy where a DNS resolver no longer sends the entire original query name to the upstream name server
Described in RFC 7816

## Slide 25: Example of QNAME Minimisation
Ask the authoritative server for a zone for the NS records of the next zone:
  Hi Root server, I want to know the nameservers for com
  Sure, here are the servers for .com

## Slide 26: Example of QNAME Minimisation
Ask the authoritative server for a zone for the NS records of the next zone:
  Hi Root server, I want to know the nameservers for com
  Sure, here are the servers for .com
  Hi .com server, I want to know the nameservers for example.com
  Sure, here are the servers for example.com

## Slide 27: Example of QNAME Minimisation
Ask the authoritative server for a zone for the NS records of the next zone:
  Hi Root server, I want to know the nameservers for com
  Sure, here are the servers for .com
  Hi .com server, I want to know the nameservers for example.com
  Sure, here are the servers for example.com
  Hi example.com server, I want to resolve www.example.com
  Sure – its 93.184.216.34

## Slide 28: Interception and Rewriting
The DNS is an easy target for the imposition of control over access
  Try asking for www.thepiratebay.org in Australia
  Try asking for www.facebook.com in China
  Etc etc
These days interception systems typically offer an incorrect response
How can you tell is the answer that the DNS gives you is the genuine answer or not?

## Slide 29: DNSSEC
DNSSEC is defined in RFCs 4033, 4034 & 4035
  Adds a number of new RRtypes that allow a digital signature to be attached to RRsets in a zone and to define how keys that are used to generate signatures are also stored in the zone
DNSSEC validation of the DNS response can tell you if the response is genuine or if it is out of date or has been altered
DNSSEC can’t tell you what the “good” answer is, just that the answer you got was not it!
DNSSEC will also tell if is an NXDOMAIN response is authentic

## Slide 30: DNSSEC and Recursive Resolvers
A DNS response that has been modified will fail to validate.
  When:
    a client asks a security-aware resolver to resolve a name, and
    sets the EDNS(0) DNSSEC OK bit, and
    the zone is DNSSEC-signed
  then the recursive resolver will only return a RRset for the query if it can validate the response using the attached digital signature
  It will set the AD bit in the resolver response to indicate validation success
  Otherwise it will return SERVFAIL
But SERVFAIL is not the same as “I smell tampering”
Its ”nope, I failed. Try another resolver”

## Slide 31: DNSSEC and Recursive Resolvers
If you are going to use a DNSSEC-validating recursive resolver
  Such as 1.1.1.1, 8.8.8.8, 9.9.9.9 or any other validating open resolver
Then make sure that all your resolvers perform DNSSEC validation if you don’t want to be mislead
  Because SERVFAIL from a validating resolver means “try the next resolver in your resolver list”

## Slide 32: DNSSEC in Spain

## Slide 33: DNSSEC in Spain

## Slide 34: DNSSEC in Portugal

## Slide 35: Negative Chattiness
Names that do not exist in the DNS are also passed to the authoritative servers in order to return the NXDOMAIN response
Sometimes the questions we ask are informative, whether or not the DNS gives an answer

## Slide 36: Aggressive NSEC Caching
Described in RFC 8198
When a zone is DNSSEC-signed an authoritative server will answer a query for a non-existent name with an authenticated denial of existence response (NSEC or NSEC3)
These records describe two adjacent labels in the zone that span the non-existent record
If recursive resolvers cache the NSEC span record then they can answer subsequent queries for any label within the span without passing the specific query onward for the cache lifetime of the NSEC record

## Slide 37: Aggressive NSEC caching
It’s a tool for recursive resolvers
Stops queries for non-existent names always heading to the zone authoritative servers
Improves the efficiency of the resolver’s cache

## Slide 38: Middleware and WireTapping
Protecting the content of DNS responses is part of what we need to make the DNS more robust
If we want to prevent DNS inspection we also should look at encrypting the transport used by DNS queries and responses
Today the standard tool is TLS, which uses dynamically generated session keys to encrypt all traffic between two parties
We could use TLS between the end client and the client’s recursive resolver
  It’s more challenging to use encryption between recursive resolvers and authoritative servers

## Slide 39: DNS over DTLS
DTLS is a UDP variant of TLS that is intended to work over UDP rather than TCP (RFC 8094)
However:
  DTLS is intolerant of fragmentation
  It appears to have similar overheads to TLS
  I’m not sure if there are any implementations of DNS over DTLS

## Slide 40: DNS over TLS
TLS is a TCP ‘overlay’ that adds server authentication and session encryption to TCP
TLS uses an initial handshake to allow a client to:
  Validate the identity of the server
  Negotiate a session key to be used in all subsequent packets in the TCP session
RFC 7858, RFC 8310
TLS 1.2 handshake

## Slide 41: DNS over TLS
Similar to DNS over TCP:
  Open a TLS session with a recursive resolver
  Pass the DNS query using DNS wireline format
  Wait for the response
Can use held DNS sessions to allow the TLS session to be used for multiple DNS queries
The queries and the responses are hidden from intermediaries
The client validates the recursive resolver’s identity

## Slide 42: DNS over TLS and Android
https://android-developers.googleblog.com/2018/04/dns-over-tls-support-in-android-p.html

## Slide 43: DNS over TLS
Will generate a higher recursive resolver memory load as each client may have a held state with one or more recursive resolvers
The TCP session state is on port 853
  DNS over TLS can be readily blocked by middleware
The privacy is relative, as the recursive resolver still knows all your DNS queries
Supported by Bind (stunnel), Unbound, DNSDist

## Slide 44: DNS over QUIC
QUIC is a transport protocol originally developed by Google and passed over to the IETF for standardised profile development
QUIC uses a thin UDP shim and an encrypted payload
  The payload is divided into a TCP-like transport header and a payload
The essential difference between DOT and DOQ is the deliberate hiding of the transport protocol from network middleware with the use of QUIC
No known implementations of DNS over QUIC exist, though IETF work continues
draft-huitema-quic-dnsoquic-05
DNS
TLS
TCP
IP
DNS
QUIC
UDP
IP
DOT
DOQ

## Slide 45: DNS over HTTPS
DNS over HTTPS
Uses an HTTPS session with a resolver
Similar to DNS over TLS, but with HTTP object semantics
Uses TCP port 443, so can be masked within other HTTPS traffic
Can use DNS wireformat or JSON format DNS payload

## Slide 46: DNS within the Browser
Firefox’s “Trusted Recursive Resolver”
Avoids using the local DNS resolver library and local DNS infrastructure
Has the browser sending its DNS queries directly to a trusted resolver over HTTPS
Servers available from Cloudflare, Google, Cleanbrowsing

## Slide 47: Push DNS
HTTPS allows server push objects as well as pull/get methods
This can allow a web page to push a DNS result to the client without the client performing a query
There is no need for these DNS names to be separately defined by conventional DNS queries
Raises possibilities for segmented namespaces

## Slide 48: DIY DNS
Run your own resolver
  The issue here is limited opportunity for caching, which means that performance could be painful!
Run your own validating stub resolver
  Getdns API interface
  Stubby stub resolver
  Still need to select a recursive resolver, but allows the local resolver to perform its own DNSSEC validation

## Slide 49: EDNS(0) Client Subnet
There is a current debate between CDN operators that rely on customized DNS responses to perform content steering, and the use of large scale open resolvers that so not necessarily preserve locality
The result is that the CDN operators wanted the client’s subnet embedded in the query to ensure that the CDN could provide enhanced content steering for the client
This has raised a number of concerns about DNS privacy
There is a forming consensus that Client Subnet has been a step too far in terms of potential privacy leakage into the DNS

## Slide 50: Choose your resolver carefully
The careful choice of an open recursive resolver and an encrypted DNS session will go a long way along the path of DNS privacy
But the compromise is that you are sharing your activity profile with the recursive resolver operator

## Slide 51: My (current) DNS Config
I use DNS over HTTPS
  I have configured Cloudflare’s Cloudflared * to listen of localhost:53
  I have set up my local /etc/resolv.conf to contain 127.0.0.1
  All my DNS queries leave my laptop in an HTTPS port 443 stream towards 1.1.1.1
* https://developers.cloudflare.com/1.1.1.1/dns-over-https/cloudflared-proxy/

## Slide 52
Thanks!