## Slide 1: Routing in 2018
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Through the Routing Lens …
There are very few ways to assemble a single view of the entire Internet
The lens of routing is one of the ways in which information relating to the entire reachable Internet is bought together
Even so, its not a perfect lens, but it can provide some useful insights about the entire scope of the Internet

## Slide 3
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Consumer Market
2011: Address Exhaustion
25 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 4: 2016-2018 in detail

## Slide 5: 2016-2018 in detail
average growth trend
Route Views Peers
RIS Peers

## Slide 6: Routing Indicators for IPv4
Routing prefixes – growing by some 52,000 prefixes per year
AS Numbers– growing by some 3,400 prefixes per year

## Slide 7: Routing Indicators for IPv4
More Specifics are still taking up slightly more than one half of the routing table
But the average size of a routing advertisement continues to shrink

## Slide 8: Routing Indicators for IPv4
Address Exhaustion is now visible in the extent of advertised address space
The “shape” of inter-AS interconnection appears to be relatively steady

## Slide 9: AS Adjacencies (AS131072)
4,144 AS6939 HURRICANE - Hurricane Electric, Inc., US
4.032 AS3356 LEVEL3 - Level 3 Communications, Inc., US
3,702 AS174 COGENT-174 - Cogent Communications, US
1,724 AS6461 ZAYO Bandwidth, US
1,646 AS7018 ATT-INTERNET4 - AT&T Services, Inc., US
1,618 AS3549 LVLT – Level 3 Parent, US
1,428 AS3257 GTT-Backbone, DE
1,377 AS2914 NTT America, US
1,208 AS209 CENTURYLINK, US
957 AS701 Verizon Business, US
51,613 out of 63,080 ASNs have 1 or 2 AS Adjacencies (82%)
1,803 ASNs have 10 or more adjacencies
9 ASNs have >1,000 adjacencies
Most networks are stub AS’s
A small number of major connectors

## Slide 10: What happened in 2018 in V4?
Routing Business as usual – despite IPv4 address exhaustion!
  From the look of the growth plots, its business as usual, despite the increasing pressures on IPv4 address availability
  The number of entries in the IPv4 default-free zone reached 750,000 by the end of 2018
  The pace of growth of the routing table is still relatively constant at ~52,000 new entries and 3,400 new AS’s per year
    IPv4 address exhaustion is not changing this!
    Instead, we appear to be advertising shorter prefixes into the routing system

## Slide 11: What about IPv4 Address Exhaustion?
ARIN – no free pool left
AFRINIC – May 2020
LACNIC – November 2019
APNIC – November 2020
RIPE NCC – January 2020
RIR Address Pool runout projections (as of April 2019):

## Slide 12: Post-Exhaustion Routing Growth
What’s driving this post-exhaustion growth?
  Transfers?
  Last /8 policies in RIPE and APNIC?
  Leasing and address recovery?

## Slide 13: Advertised Address “Age”
80% of all new addresses announced in 2010 were allocated or assigned within the past 12 months
2% of all new addresses announced in 2010 were >= 20 years ‘old’ (legacy)
2010

## Slide 14: Advertised Address “Age”
20% of all new addresses announced in 2018 were allocated or assigned within the past 12 months
48% of all new addresses announced in 2018 were >= 20 years ‘old’ (legacy)
2018

## Slide 15: 2000 – 2018: IPv4 Advertised vs Unadvertised

## Slide 16: 2000 – 2018: Unadvertised Addresses
Total volume of
“reclaimed” addresses

## Slide 17: 2018: Assigned vs Recovered
Change in Advertised Addresses
Change in the Unadvertised Address Pool
RIR Allocations
“draw down”

## Slide 18: V4 in 2018
The equivalent of 1.4 /8s were removed from the routing table across 2018
Approximately 0.86 /8s were assigned by RIRs in 2015
  0.37 /8’s assigned by Afrinic
  0.28 /8s assigned by the RIPE NCC (last /8 allocations)
  0.10 /8s were assigned by APNIC (last /8 allocations)
And a net of 2.1 /8’s were added to the pool of unadvertised addresses
In 2018 we saw legacy blocks transferring away from ISPs / end user sites and heading towards cloud SPs.

## Slide 19: The Route-Views View of IPv6
IANA IPv4 Exhaustion

## Slide 20: 2017-2018 in Detail

## Slide 21: Routing Indicators for IPv6
Routing prefixes – growing by some 15,000 prefixes per year
AS Numbers– growing by some 2,000 ASNs per year (which is 60% the V4 growth)

## Slide 22: Routing Indicators for IPv6
More Specifics now take up more than one third of the routing table
The average size of a routing advertisement is getting smaller

## Slide 23: Routing Indicators for IPv6
Advertised Address span is growing at an exponential rate
The “shape” of inter-AS interconnection in IPv6 is rising slightly. Local connections appear to be replacing overlay trunk transits

## Slide 24: AS Adjacencies (AS131072)
13,095 out of 16,465 ASNs have 1 or 2 AS Adjacencies (79%)
573 ASNs have 10 or more adjacencies
2 ASNs have >1,000 adjacencies
4,295 AS6939 HURRICANE - Hurricane Electric, Inc., US
1,049 AS3356 LEVEL3 - Level 3 Communications, Inc., US
749 AS174 COGENT-174 - Cogent Communications, US
719 AS2915 NTT America, US
632 AS1299 Telia Carrier, SE

## Slide 25: V6 in 2018
Overall IPv6 Internet growth in terms of BGP is still increasing, and is currently at some 15,000 route entries p.a.

## Slide 26: What to expect

## Slide 27: BGP Size Projections
How quickly is the routing space growing?
What are the projections of future BGP FIB size?

## Slide 28: V4 - Daily Growth Rates
Growth in the V4 network appears to be constant at a long term average of 140 additional routes per day, or some 52,000 additional routes per year

## Slide 29: V4 BGP Table Size Predictions
Jan 2017 646,000
2018 699,000
2019 755,000
2020 807,000
2021 859,000
2022 911,000
2023 963,000
2024 1,015,000

## Slide 30: V6 - Daily Growth Rates

## Slide 31: V6 BGP Table Size Predictions
Jan 2017 35,000 36,000
2018 49,000 47,000
2019 62,000 62,000
2020 75,000 83,000
2021 89,000 109,000
2022 102,000 145,000
2023 116,000 192,000
2024 130,000 255,000
Linear Exponential

## Slide 32: BGP Table Growth
The absolute size of the IPv6 routing table is growing much faster than the IPv4 table
IPv6 will require the same memory size in around 5 years time, given that each IPv6 entry is 4 times the memory size of an IPv4 entry
As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 33: BGP Updates
What about the level of updates in BGP?

## Slide 34: IPv4 BGP Updates

## Slide 35: IPv4 BGP Convergence Performance

## Slide 36: Updates in IPv4 BGP
Still no great level of concern …
The number of updates per instability event and the time to converge has been relatively constant
Likely contributors to this outcome are the damping effect of widespread use of the MRAI interval by eBGP speakers, and the compressed topology factor, as seen in the relatively constant AS Path Length

## Slide 37: V6 BGP Updates

## Slide 38: V6 Convergence Performance

## Slide 39: Routing Futures
There is little in the way of scaling pressure from BGP as a routing protocol – the relatively compressed topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet
The issues of FIB size, line speeds and equipment cost of line cards represent a more significant issue for hardware suppliers – we can expect cheaper line cards to to use far smaller LRU cache local FIBs in the high speed switches and push less used routes to a slower / cheaper lookup path. This approach may also become common in very high speed line cards

## Slide 40: Some Practical Suggestions
Understand your hardware’s high speed FIB capacity in the default-free parts of your network
Review your IPv4 / IPv6 portioning - a dual-stack eBGP router will need 900,000 IPv4 slots and 110,000 IPv6 slots for a full eBGP routing table in line cards over the coming 24 months if they are using a full FIB load
Judicious use of default routes in your internal network may allow you drop this requirement significantly

## Slide 41: That’s it!
Questions?