## Slide 1: Detecting BGP Anomalies
Geoff Huston
APNIC Labs

## Slide 2: BGP Anomaly Detection
The objective of an BGP anomaly detector is to process BGP updates and automatically detect “anomalies” where the prefix or the path does not appear to be aligned to “normal” routing behaviours
The challenge is to train an automated system to generate a useful model of “normal” and “anomalous” classification of BGP updates

## Slide 3: Approaches to Anomaly Detection
I - Rule-based systems
  Have network operators describe their routing policies
  Trigger notification on detected exceptions
  For example:
    AS131072
      Originates:
        192.0.2.0/24
        2001:DB8::/32
      Provider AS
        AS4608
      DownstreamAS:
        Nil
BGP4MP|1566349266|A|192.0.2.0/24|4608 4777 131072|IGP|
BGP4MP|1566349266|A|192.0.2.128/25|4608 4777|IGP
matches the rule set
does not matches rule set
BGP updates:

## Slide 4: Approaches to Anomaly Detection
I - Rule-based systems
  Have network operators describe their routing policies
  Trigger notification on detected exceptions
  For example:
    AS131072
      Originates:
        192.0.2.0/24
        2001:DB8::/32
      Next-Hop AS
        AS4608
      Downstream AS:
        Nil

## Slide 5: Approaches to Anomaly Detection
I - Rule-based systems
  Have network operators describe their routing policies
  Trigger notification on detected exceptions
  For example:
    AS131072
      Originates:
        192.0.2.0/24
        2001:DB8::/32
      Next-Hop AS
        AS4608
      Downstream AS:
        Nil
BGP4MP|1566349266|A|192.0.2.0/24|3556 4608 131072|IGP
BGP4MP|1566349266|A|192.0.2.0/24|3556 4823 4777 131072|IGP

## Slide 6: Approaches to Anomaly Detection
II – Machine Based Learning
  Feed updates into a parameter generator
  Perform n-dimensional cluster analysis on the data set
  Identify outliers as potential anomalies
Outliers?

## Slide 7: Approaches to Anomaly Detection
III – Heuristics
  Feed updates into an analyser
  Generate a n-dimensional ‘score’ for the update
  Use thresholds to pick out out candidate anomalies
  Which is the focus of this project…

## Slide 8: BGP is a Chatty Protocol
It’s a distance vector protocol
Which means that it converges through exhaustion via progressive refinement, not through direct computation (as is the case with SPF protocols)
Which also implies that there are transient states that are not stable
Which implies that when we look for anomalies in BGP updates there is a huge amount of BGP chaff to work through!

## Slide 9: BGP Update Profile

## Slide 10: BGP Update Profile
Over 10 years the number of prefixes has more than doubled
Number of prefix updates was stable for 4 years, then has been rising slowly
Number of prefix withdrawals has been steady

## Slide 11: BGP Update Profile
A conventional default-free IPv4 eBGP session at the edge of the Internet will process some 150,000 – 200,000 prefix announcements per day
And some 10,000 prefix withdrawals per day
This is a relatively stable profile for eBGP update activity

## Slide 12: BGP Update Profile
It is useful to understand how much of this protocol traffic is a by product of the operation of the protocol, how much is realignment of the network topology and how much is “new” reachability information
Let’s count the daily number of prefixes in the eBGP RIB and the daily count of previously unseen prefixes

## Slide 13: BGP Prefix Updates – IPv4
There are some 200-300 ”new” prefixes per day in the IPv4 BGP RIB

## Slide 14: BGP Prefix Updates – IPv6
There were some 5-10 ”new” prefixes per day in the IPv6 BGP RIB

## Slide 15: BGP AS Adjacency Updates - IPv4
There are up to 100 ”new” AS Adjacencies per day in the IPv4 BGP RIB

## Slide 16: BGP AS Adjacency Updates – V6
There are up to 30 ”new” AS Adjacencies per day in the IPv4 BGP RIB

## Slide 17: BGP Updates and Information Content
BGP updates tend to repeat previous information most of the time
  150,000 updates per day, but only 200 – 300 previously unseen prefixes and 100 previously unseen AS adjacencies per day
The “new” information content volume in BGP updates is relatively small, and is scale free
  (The rate of growth is not directly related to the size of the network)
If we use “new” information as a trigger point to look for unusual BGP activity we might have a useful way to filter BGP updates

## Slide 18: BGP Update Processing
For each Prefix, load the prefix into an aggregate and more specific context tree
For each AS Path, analyse the AS ordered adjacencies and infer the provider / peer / customer relationship
Geolocate the prefix and the originating AS
Check the ROA status
Check the IRR material for this prefix
Now apply an anomaly “interest” level calculation on announcement and withdrawal

## Slide 19: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
  The AS at the trough of the valley is leaking routes from one upstream provider to another
Leak!
customer
transit provider

## Slide 20: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
  The AS path is synthetic and is not a BGP generated ‘history’ of the propagation of the update
  It could be a poison AS to deflect traffic for TE
  Or an effort to create a false ‘best path’ to redirect traffic

## Slide 21: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
  Address hijack?
  Bogon?

## Slide 22: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
Previously unseen ASes
  Fake AS Path?
  AS hijack?

## Slide 23: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
Previously unseen ASes
Prefixes that are more specifics or aggregates where the origin ASs are different
  “Hole punching”
  Or route hijack by more specifics

## Slide 24: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
Previously unseen ASes
Prefixes that are more specifics or aggregates where the origin ASs are different
Prefixes where the geolocation of the more specifics are different
  “Hole punching”
  Or route hijack by more specifics

## Slide 25: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
Previously unseen ASes
Prefixes that are more specifics or aggregates where the origin ASs are different
Prefixes where the geolocation of the more specifics are different
Prefixes where the geolocation of the prefix and the Originating AS are different
  route hijack?

## Slide 26: What is “interesting” in BGP Updates?
AS paths that contain “valleys”
AS paths that contain ASes in “unusual” places
Previously unseen prefixes
Previously unseen ASes
Prefixes that are more specifics or aggregates where the origin ASs are different
Prefixes where the geolocation of the more specifics are different
Prefixes where the geolocation of the prefix and the Originating AS are different
Short lived prefixes
  After “a period” its no longer an anomaly but part of the set of BGP ground truths

## Slide 27: Interest and Intent Filtering
RPKI can be interpreted as a strong statement of routing intent
IRR data can also be interpreted as intent, although without the same level of clarity of intent
More specific announcement floods are “interesting”

## Slide 28: This Project
Yet another BGP Anomaly detector
Why another?
  Open source code base (C )
  Generic design that can cope with feeds from one or more BGP speakers
  Intended to use plug in filter sets, to allow both specific rule applications and more general anomaly detection

## Slide 29: Overall Architecture
Input module
RIB Model
RPKI Filter
IRR Filter
AS valley Filter
Rule Filter
Classifier
Anomalous update feed

## Slide 30: Reporting
How should the tool report?
  JSON feed
  Web Archive
  Linked into RIPEStat
  Other report formats?

## Slide 31: Current Status
Flikr: P.A.H. http://bit.ly/320TEF4

## Slide 32: Interested in this work?
You can play too:
Pass an eBGP feed to a detector
Take a copy of the code and apply it to your own BGP feeds?
Subscribing to a BGP anomaly feed service using your rule set
Interested in subscribing to a general BGP anomaly feed

## Slide 33: APNIC’s Role
We share an interest in a secure and stable routing system
We’d like to help operators by informing them of the status of routing stability
We are interested in trying to measure the incidence of BGP anomalies over time to inform the community about the severity and incidence of these anomalies

## Slide 34: Thanks!