## Slide 1: 30 Years of BGP
A Lesson in Protocol Evolution
Geoff Huston
APNIC

## Slide 2: In the Beginning…
BGP was an evolution of the earlier EGP protocol (developed in 1982 by Eric Rosen and Dave Mills)
BGP-1 – RFC 1105, June 1989, Kirk Lougheed, Yakov Rekhter
  TCP-based message exchange protocol, based on distance vector routing algorithm with explicit path attributes
BGP-3 – RFC1267, October 1991, Kirk Lougheed, Yakov Rekhter
  Essentially a clarification and minor tweaks to the basic concepts used in BGP
BGP-4 – RFC 1654, July 1994, Yakov Rekhter, Tony Li
  Added CIDR (supporting explicit prefix lengths) and proxy aggregation

## Slide 3: I - The Protocol Design of BGP

## Slide 4: Routing Hierarchies
Earlier protocols, notably DECnet Phase IV, supported scaling by hierarchies:
  Within an “area” the routing protocol maintained a detailed topology that allowed all nodes within the area to reach any other node in the same area using links that were managed by the inter-area routing protocol
  Area border routers maintained an inter-area topology
BGP borrowed this concept, using the terminology of “Autonomous Systems” in a manner similar to the concept of “areas”
Unlike DECnet, BGP did not define the ”interior” routing protocol, decoupling the concepts of internal and exterior routing in this two-level hierarchy

## Slide 5: Routing Hierarchies
Earlier protocols, notably DECnet Phase IV, supported scaling by hierarchies:
  Within an “area” the routing protocol maintained a detailed topology that allowed all nodes within the area to reach any other node in the same area using links that were managed by the inter-area routing protocol
  Area border routers maintained an inter-area topology
BGP borrowed this concept, using the terminology of “Autonomous Systems” in a manner similar to the concept of “areas”
Unlike DECnet, BGP did not define the ”interior” routing protocol, decoupling the concepts of internal and exterior routing in this two-level hierarchy
Lesson:
Don’t try to solve everything – underachieving can be a virtue!

## Slide 6: BGP Protocol
BGP is a message passing protocol layered above TCP
TCP manages:
  Framing of individual elements of the protocol exchange
  Reliability of the exchange
  Flow control, including rate adaptation
BGP assumes that as long as the TCP session remains up then everything that was passed to a peer is known by that peer for the duration of the session
  BGP need only send changes, without periodic refresh for the lifetime of the session

## Slide 7: BGP Protocol
BGP is a message passing protocol layered above TCP
TCP manages:
  Framing of individual elements of the protocol exchange
  Reliability of the exchange
  Flow control, including rate adaptation
BGP assumes that as long as the TCP session remains up then everything that was passed to a peer is known by that peer for the duration of the session
  BGP need only send changes, without periodic refresh for the lifetime of the session
Lessons:
Reuse, don’t re-invent!
Don’t duplicate functionality

## Slide 8: BGP and Packet Forwarding
BGP does not alter IP packets
  Its role is to inform routers on how to make forwarding decisions
IP packets do not contain AS information
  The association of IP addresses to an AS is a BGP concept. Within an AS, the interior routers and interior routing protocols and hosts have no knowledge of the local AS.
  Which makes network rehoming in the AS space easy
  Which prevents provider lock-in and aids in a competitive supply for transit

## Slide 9: BGP and Packet Forwarding
BGP does not alter IP packets
  Its role is to inform routers on how to make forwarding decisions
IP packets do not contain AS information
  The association of IP addresses to an AS is a BGP concept. Within an AS, the interior routers and interior routing protocols and hosts have no knowledge of the local AS.
  Which makes network rehoming in the AS space easy
  Which prevents provider lock-in and aids in a competitive supply for transit
Lessons:
Focus focus focus!
Limit side-effects as much as possible

## Slide 10: BGP Policy
Each AS can determine its own traffic export policy autonomously
  Within some constraints
The AS Path concept was primarily there to prevent loops, nothing more
BGP will by default prefer to use the shortest AS path
  It’s a crude LCD metric
  But if the network admin wants to use some other route selection policy framework, then BGP won’t stop you!
Local BGP policy is opaque
  Whatever your BGP policy settings may be, they are your policy settings, and no one else needs to know them!
  What you accept from your peers and what you choose to re-advertise to your peers and why is your call and your business

## Slide 11: BGP Policy
Each AS can determine its own traffic export policy autonomously
  Within some constraints
The AS Path concept was primarily there to prevent loops, nothing more
BGP will by default prefer to use the shortest AS path
  It’s a crude LCD metric
  But if the network admin wants to use some other route selection policy framework, then BGP won’t stop you!
Local BGP policy is opaque
  Whatever your BGP policy settings may be, they are your policy settings, and no one else needs to know them!
  What you accept from your peers and what you choose to re-advertise to your peers and why is your call and your business
Lesson:
Don’t make the protocol force the business model

## Slide 12: BGP is Non-Deterministic
(Which is an odd property of a routing protocol!)
BGP is best seen as a negotiation protocol, attempting to find a point of equilibrium between networks’ export and import policies
Subtle changes in timers and sequencing of BGP update processing means that the routing outcomes are not necessarily deterministic.

## Slide 13: BGP is Non-Deterministic
(Which is an odd property of a routing protocol!)
BGP is best seen as a negotiation protocol, attempting to find a point of equilibrium between networks’ export and import policies
Subtle changes in timers and sequencing of BGP update processing means that the routing outcomes are not necessarily deterministic.
Lesson:
Don’t be OCD – any solution is still a solution!

## Slide 14: Why has BGP lasted?
Don’t try to solve everything – underachieving can be a virtue!
Reuse, don’t re-invent
Don’t duplicate functionality
Focus focus focus! Limit side-effects as much as possible
Don’t make the protocol force the business model
Don’t be OCD – any solution is still a solution!

## Slide 15: II - BGP Deployment Experience

## Slide 16: Containing the Routing “Explosion”
IETF ROAD Efforts in 1992 (RFC1380)
  Predicted exhaustion of IPv4 addresses and scaling explosion of inter-domain routing
The chosen “solution” was to drop the concept of address classes from BGP
It (sort of) worked for a while
  Until it didn’t!
0
1993
1995

## Slide 17: IPv6 and BGP
While the IETF adopted the IPv6 address architecture for the address exhaustion issue, it was unable to find an IPv6 routing architecture that had similar scaling properties
  IETF efforts to impose a routing hierarchy (TLAs and sub-TLAs – RFC 2928) got nowhere!
So we just used BGP for IPv6 in the same way as we used BGP for IPv4
  Address allocation policies that allocated ‘independent’ address blocks of /35 or larger
  ISP traffic engineering and hijack “defence” by advertising more specifics

## Slide 18: BGP and TE
BGP cannot load-balance in the inter-AS space
  It’s a ‘winner-take-all’ best path selection protocol
  It cannot load balance as it has no concept of feedback loops
BGP cannot perform traffic engineering easily
  Because routing policies are intrinsically non-transitive and AS prepending is completely unreliable, the only leverage left to engineer traffic is the selective advertisement of more specific routes
  Which means that BGP carries large volumes of more specific routes whose primary purpose appears to relate to various efforts to perform traffic engineering of incoming traffic

## Slide 19: BGP Scaling
BGP has scaled because the protocol only passes topology deltas - as long as the topology change rate is low, the BGP load is low
The strongly clustered inter-AS topology of the Internet works in BGP’s favour
BGP has grown well beyond any original design expectations

## Slide 20: But - Scale generates Inertia
BGP-4 was introduced when the routing table contained ~ 10K entries – it is now ~800K entries and carries some 75K ASNs
This has its own inertial mass that resists change
Changing the routing environment to use a new IDR protocol would be incredibly challenging, even if we understood what we wanted from any candidate successor IDR protocol

## Slide 21: Expectations vs Deployment
Session lifetime
  Expectations of short session lifetimes – experience of session longevity
Session Security
  Expectation of routing being a public function - experience of session attack
Payload Integrity
  Expectations of mutual trust – experience of malicious and negligent attack
Protocol Performance
  Expectations of slow performance – experience of more demanding environments
Error Handling
  Expectations of “clear session” as the universal solution – experience required better recovery without catastrophic session teardown
Use
  Expectations of simple topology maintenance – experience of complex traffic engineering

## Slide 22: Deployment: BGP isn’t perfect
Session insecurity
Payload insecurity
Protocol instability
Sparseness of signalling
No ability to distinguish between topology maintenance, policy negotiation and traffic engineering

## Slide 23: III - Where should we go with BGP?

## Slide 24: Incremental tweaking?
Which as what we’ve been doing for 30 years:
  Capability negotiation
  Add Path
  Extended communities
  Fast BGP
  Graceful Restart
  4-byte AS’s
  …

## Slide 25: Does tweaking “work”?
Not Really
There are few BGP tweaks that provide substantial benefit to adopters in partial deployment scenarios in the Internet
  Routing is a universal substrate and deviations from a common model are necessarily limited in scope and impact in order to interoperate with the common mass of behaviour
As long as tweaks are localised in both impact and benefit they find it hard to gather sufficient impetus to impel common adoption
  There are exceptions to this - like 4 byte ASN – but they are exceptions to the common behaviour model

## Slide 26: Time for a ”new” IDR?
What? Not again!
We’ve been here before many times:
  “BGP is failing because <reasons> and we need to shift to a new IDR for the Internet”
We have no new basic insights into routing in a diverse multi-provider space
  Which means that we have no real assurance that we could improve on the basic BGP functions
  “

## Slide 27: Lessons from 30 years of BGP
Enduring use is often an accidental and unintended outcome
Simplicity is often undervalued
Hop-by-Hop protocols are extremely flexible
TCP is more powerful than anyone thought!
Its by no means a perfect solution but it represents a set of compromises that we are willing to accept

## Slide 28: What about the next 30 years?
I just don’t know!

## Slide 29: What about the next 30 years?
I just don’t know!
There are major issues with content delivery systems and a major tension between carriage and content
  In the multi-provider carriage environment BGP has a clear role to play for the near term future
  In a future uni-provider content delivery system there are other approaches that can deliver better outcomes, incorporating feedback systems to support load balancing and adding fine-grained traffic steerage
  So which way are we heading with the Internet?

## Slide 30: What about the next 30 years?
I just don’t know!
There are major issues with content delivery systems and a major tension between carriage and content
  In the multi-provider carriage environment BGP has a clear role to play for the near term future
  In a future uni-provider content delivery system there are other approaches that can deliver better outcomes, incorporating feedback systems to support load balancing and adding fine-grained traffic steerage
  So which way are we heading with the Internet?
The entire Internet may change and make BGP and IDR itself irrelevant! But that form of change is WAY more than just a discussion about BGP and routing!

## Slide 31: Will it get better?
Will we ever secure BGP?
Will we clear out bogons?
What about more specifics?
Stop senseless prepending?
See an end to massive route leaks?

## Slide 32: Will it get better?
Will we ever secure BGP?
Will we clear out bogons?
What about more specifics?
Stop senseless prepending?
See an end to massive route leaks?
Nope!

## Slide 33: My Opinions
We’re not going to change BGP anytime soon:
  It’s still functional
  We’ve grown used to working with its strengths and we’ve become accustomed to avoiding or tolerating its weaknesses
  Its adequately efficient
  The business model and the BGP model have managed to come to terms with each other
  The levels of abuse are tolerable (so far)
  And we’ve trained a large body of network operators who understand how to drive / abuse it for fun and profit!
  And we have no plan B!

## Slide 34: Thanks!