## Slide 1: The Routing and Addressing in the Internet – 2019 in Review
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Through the Routing Lens …
There are very few ways to assemble a single view of the entire Internet
The lens of routing is one of the ways in which information relating to the entire reachable Internet is bought together
Even so, its not a perfect lens, but it can provide some useful insights about the entire scope of the Internet

## Slide 3
1994: Introduction of CIDR
2001: The Great Internet
Boom and Bust
2005: Consumer Market
2011: Address Exhaustion
25 Years of Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 4: 2017-2019 in detail

## Slide 5: 2017-2019 in detail
average growth trend
Route Views Peers
RIS Peers

## Slide 6: Routing Indicators for IPv4
Routing prefixes – growing by some 51,000 prefixes per year
AS Numbers– growing by some 3,400 prefixes per year

## Slide 7: Routing Indicators for IPv4
More Specifics are still taking up slightly more than one half of the routing table
But the average size of a routing advertisement continues to shrink

## Slide 8: Routing Indicators for IPv4
Address Exhaustion is now visible in the extent of advertised address space
The “shape” of inter-AS interconnection appears to be relatively steady

## Slide 9: AS Adjacencies (AS131072)
4,498 AS6939 HURRICANE - Hurricane Electric, Inc., US
4,291 AS3356 LEVEL3 - Level 3 Communications, Inc., US
3,947 AS174 COGENT-174 - Cogent Communications, US
1,803 AS6461 ZAYO Bandwidth, US
1,722 AS3257 GTT-Backbone, DE
1,649 AS7018 ATT-INTERNET4 - AT&T Services, Inc., US
1,422 AS2914 NTT America, US
1,377 AS3549 LVLT – Level 3 Parent, US
1228 AS1299 TELIANET Telia Carrier, SE
1,148 AS209 CENTURYLINK, US
54,697 out of 66,928 ASNs have 1 or 2 AS Adjacencies (82%)
2,195 ASNs have 10 or more adjacencies
10 ASNs have >1,000 adjacencies
Most networks are stub AS’s
A small number of major connectors

## Slide 10: What happened in 2019 in V4?
Routing Business as usual – despite IPv4 address exhaustion!
  From the look of the growth plots, its business as usual, despite the increasing pressures on IPv4 address availability
  The number of entries in the IPv4 default-free zone reached 800,000 by the end of 2019
  The pace of growth of the routing table is still relatively constant at ~51,000 new entries and 3,400 new AS’s per year
    IPv4 address exhaustion is not changing this!
    Instead, we appear to be advertising shorter prefixes into the routing system

## Slide 11: What about IPv4 Address Exhaustion?
ARIN – no free pool left
AFRINIC – July 2020
LACNIC – no free pool left
APNIC – January 2021
RIPE NCC – no free pool left
RIR Address Pool runout projections as of the start of 2020:

## Slide 12: Post-Exhaustion Routing Growth
What’s driving this post-exhaustion growth?
  Transfers?
  Last /8 policies in RIPE and APNIC?
  Leasing and address recovery?

## Slide 13: Advertised Address “Age”
80% of all new addresses announced in 2010 were allocated or assigned within the past 12 months
2% of all new addresses announced in 2010 were >= 20 years ‘old’ (legacy)
2010

## Slide 14: Advertised Address “Age”
2019
Re-use of legacy addresses
transfers

## Slide 15: 2000 – 2019: IPv4 Advertised vs Unadvertised

## Slide 16: 2005 – 2020: Unadvertised Addresses

## Slide 17: 2019: Assigned vs Recovered
Change in Advertised Addresses
Change in the Unadvertised Address Pool
RIR Allocations
Advertised growth
Unadvertised growth

## Slide 18: V4 in 2019
The equivalent of 0.4 /8s were added to the routing table across 2019
Approximately 2.5 /8s were assigned by RIRs in 2019
  0.38 /8s assigned by the RIPE NCC (last /8 allocations)
  0.27 /8’s assigned by Afrinic
  0.09 /8s were assigned by LACNIC
  0.06 /8s were assigned by APNIC (last /8 allocations)
  1.7 /8s assigned by ARIN (transfers)
And a net of 2.1 /8’s were added to the pool of unadvertised addresses
In 2019 we saw legacy blocks transferring away from ISPs / end user sites and heading towards cloud SPs.

## Slide 19: The Route-Views View of IPv6
IANA IPv4 Exhaustion

## Slide 20: 2018-2019 in Detail

## Slide 21: Routing Indicators for IPv6
Routing prefixes – growing by some 17,000 prefixes per year
AS Numbers– growing by some 2,000 ASNs per year (which is 60% the V4 growth)

## Slide 22: Routing Indicators for IPv6
More Specifics now take up one half of the routing table
The average size of a routing advertisement is getting smaller

## Slide 23: Routing Indicators for IPv6
Advertised Address span is growing at an exponential rate
The “shape” of inter-AS interconnection in IPv6 is rising slightly. Local connections appear to be replacing overlay trunk transits

## Slide 24: AS Adjacencies (AS131072)
14,997 out of 18,720 ASNs have 1 or 2 AS Adjacencies (80%)
654 ASNs have 10 or more adjacencies
2 ASNs have >1,000 adjacencies
4,728 AS6939 HURRICANE - Hurricane Electric, Inc., US
1,011 AS3356 LEVEL3 - Level 3 Communications, Inc., US
955 AS174 COGENT-174 - Cogent Communications, US
948 AS1299 Telia Carrier, SE
818 AS2914 NTT America, US

## Slide 25: V6 in 2018
Overall IPv6 Internet growth in terms of BGP is still increasing, and is currently at some 17,000 route entries p.a.

## Slide 26: What to expect

## Slide 27: BGP Size Projections
How quickly is the routing space growing?
What are the projections of future BGP FIB size?

## Slide 28: V4 - Daily Growth Rates
Growth in the V4 network appears to be constant at a long term average of 150 additional routes per day, or some 51,000 additional routes per year

## Slide 29: V4 BGP Table Size Predictions
Jan 2017 646,000
2018 699,000
2019 760,000
2020 814,000
2021 862,000
2022 916,000
2023 970,000
2024 1,024,000
2025 1,079,000

## Slide 30: V6 - Daily Growth Rates

## Slide 31: V6 BGP Table Size Predictions
Jan 2017 35,000
2018 45,000
2019 62,000
2020 75,000
2021 96,000 106,000
2022 112,000 140,000
2023 128,000 184,000
2024 144,000 242,000
2025 160,000 318,000
Linear Exponential

## Slide 32: BGP Table Growth
The absolute size of the IPv6 routing table is growing much faster than the IPv4 table
They will require the same memory size in around 5 years time, given that each IPv6 entry is 4 times the memory size of an IPv4 entry
As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet

## Slide 33: BGP Updates
What about the level of updates in BGP?

## Slide 34: IPv4 BGP Updates

## Slide 35: IPv4 BGP Convergence Performance

## Slide 36: Updates in IPv4 BGP
Still no great level of concern …
The number of updates per instability event and the time to converge has been relatively constant
Likely contributors to this outcome are the damping effect of widespread use of the MRAI interval by eBGP speakers, and the compressed topology factor, as seen in the relatively constant AS Path Length

## Slide 37: V6 BGP Updates

## Slide 38: V6 Convergence Performance

## Slide 39: V6 Convergence Performance

## Slide 40: Routing Futures
There is little in the way of scaling pressure from BGP as a routing protocol – the relatively compressed topology and stability of the infrastructure links tend to ensure that BGP remains effective in routing the internet
The issues of FIB size, line speeds and equipment cost of line cards represent a more significant issue for hardware suppliers – we can expect cheaper line cards to to use far smaller LRU cache local FIBs in the high-speed switches and push less-used routes to a slower / cheaper lookup path. This approach may also become common in very high-capacity line cards

## Slide 41: Some Practical Suggestions
Understand your hardware’s high speed FIB capacity in the default-free parts of your network
Review your IPv4 / IPv6 portioning - a dual-stack eBGP router will need 920,000 IPv4 slots and 140,000 IPv6 slots for a full eBGP routing table in line cards over the coming 24 months if they are using a full FIB load
Judicious use of default routes in your internal network may allow you drop this requirement significantly
Using a hot cache for line card FIB cache would reduce the memory requirement significantly without visible performance cost

## Slide 42: That’s it!
Questions?