## Slide 1: Measurement of IPv6 Extension Header Support
Geoff Huston
APNIC Labs

## Slide 2
IPv6 Extension Header
The extension header sits between the IPv6 packet header and the upper level protocol header for the leading fragged packet, and sits between the header and the trailing payload frags for the trailing packets
Practically, this means that transport-protocol aware packet processors/switches need to decode the extension header chain, if its present, which can consume additional cycles to process/switch a packet – and the additional time is not predictable. For trailing frags there is no transport header!
Or the unit can simply discard all IPv6 packets that contain extension headers - which is what a lot of transport protocol sensitive IPv6 deployed switching equipment appears to do!
IPv6 header
Payload
TCP/UDP header
Xtn header

## Slide 3
RFC 7872
test station
tested servers
?
Request (with EH options)
June 2016
One-to-many test sending sets of well-known servers requests where EH options are added to the outbound packets
The test is whether or not the server sends a response
Tested Destination Options, Hop-by-hop and Fragments

## Slide 4
IPv6 EH Fragmentation Handling
There is a lot of “drop” behaviour in the IPv6 Internet for Fragmentation Extension headers
  RFC7872 – recorded EH packet drop rates of 30% - 55%
But sending fragmented queries to servers is not all that common – the reverse situation of big responses is more common
So what about sending fragmented packets BACK from servers – what’s the drop rate of the reverse case?

## Slide 5: Our Measurement Approach
We use an Online Ad platform to enroll endpoints to attempt to resolve a set of DNS names:
  Each endpoint is provided with a unique name string (to eliminate the effects of DNS caching)
  The DNS name is served from our authoritative servers
  Resolving the DNS name requires the user’s DNS resolvers to receive a fragmented IPv6 packet
tested clients
tested server
?

## Slide 6: “Glueless” Delegation to detect IPv6 Fragmentation Handling
“Parent” name server
“Sibling” name server
“Child” name server
The “child” name server will only be queried if the resolver could receive the response from the sibling name server
Reply with the DNS names of the name servers, but not their IP addresses
Secondary objective: resolve these
name server names to their IP addresses
Resume the original name resolution task
Use a modified DNS server that fragments all DNS responses

## Slide 7: V6, the DNS and Fragmented UDP
Total number of tests: 10,851,323
Failure Rate in receiving a large response: 4,064,356
IPv6 Fragmentation Failure Rate: 38%
2017 data

## Slide 8: V6, the DNS and Fragmented UDP
Total number of tests: 27,619,047
Failure Rate in receiving a large response: 11,232,833
IPv6 Fragmentation Failure Rate: 41%
2020 data

## Slide 9: Which Resolvers?
10,115 IPv6 seen resolvers
3,592 resolvers were consistently unable to resolve the target name (likely due to failure to receive the fragmented response)
Which is too large a list to display here
But we can show the top 20…

## Slide 10: Which Resolvers?
All these resolvers appears to be unable to receive fragmented UDP
DNS responses – This is the Top 20, as measured by the query count
per resolver address

## Slide 11: Resolvers in Which Networks?
This is the total per origin AS of those resolvers that appear to be unable to receive fragmented UDP DNS responses. This is the Top 20, as measured by the query count per origin AS

## Slide 12: What about TCP and the IPv6 Fragmentation Header?
Let’s try the same approach:
  Set up an ad-based measurement using a customised IPv6 packet handler
  Pass all TCP responses through a packet fragmenter
    Use an IPv6 NAT-66 implementation that takes a server’s IPv6 packets and wrangles them to include an EH header before passing them back to the client
    In this case any packet with size > 512 octets was mangled to fragment at a 512 octets
  Use a packet capture to see if the fragmented TCP segment was ACKed or not
end host
IPv6 server
NAT-66
EH insertion

## Slide 13: What about TCP and IPv6 Fragmentation?
1,961,561 distinct IPv6 end point addresses
434,971 failed to receive Fragmented IPv6 packets
22% failure rate

## Slide 14: Where are TCP e-2-e drops?
Top 15 networks with highest Fragmented IPv6 Drop Rates

## Slide 15: Why do we see these high packet drop rates?
Two major factors appear to lie behind this failure rate:
  Network equipment dropping IPv6 packets with Extension Headers
  Firewalls dropping Fragmented packets

## Slide 16: Next Measurement Steps?
Test other Extension Headers
Hop-by-Hop Extension headers
Destination Extension Headers
Compare TCP and UDP drop performance
Locate Drop Point
at end point?
in flight?

## Slide 17: But
Can we fix the network anyway?
  Or is this just an exercise in trying to make the pig fly?

## Slide 18: Or
Like the fate of IPv4 options, just forget about using them, and declare IPv6 EH headers a bad idea!

## Slide 19: Or, but
If we forget about IPv6 EH then IPv6 fragmentation is no longer possible
And that will put a huge strain on IPv6 UDP applications
Like the DNS!
  And we really don’t have a good answer for that so far!

## Slide 20: What’s the real question here?
What else do we need to understand about networks and end stack behaviours in IPv6 in order to figure out whether to abandon EH completely or try to salvage bits of it and make those bits work everywhere?

## Slide 21
Thanks!