## Slide 1
IP Technology Adoption in Bhutan
Geoff Huston
APNIC Labs

## Slide 2: Why?
Bhutan has a really high rate of adoption of DNSSEC in their recursive resolvers
And a decent rate of RoV ROA filtering for BGP
And a close to perfect rate of signed ROAs in their address infrastructure
Yet …
Not much IPv6!

## Slide 3: Bhutan is not that unusual
Many national environments have a unique technology adoption profile across these 4 technologies:
DNSSEC IPv6 ROA Signing RoV Filtering
Bhutan high not much perfect decent
Sweden high not much not really good
Brazil high decent nope none
Spain low not much decent none
India high huge decent not much
US so-so good decent so-so
Mongolia high nope perfect! good

## Slide 4: Sameness and Differences
All these markets have a similar technology base for consumers
And they all use equipment drawn from a similar pool of vendors
And the supply costs are largely the same across the entire network
Yet…
They have different consumer “wealth” indicators
There are different technology deployment models in each national market
Though relative wealth and technology choices do not correlate well!

## Slide 5: Lets look at each technology in a little more detail

## Slide 6: IPv6 Adoption - 2014 to Today
28% of the Internet’s user base have IPv6 today

## Slide 7: Europe is (slightly) lagging…
23% of the Europe’s user base have IPv6 today

## Slide 8: And is very diverse
IPv6 is deployed in Central
Europe and Greece, but not in
the North, South or East

## Slide 9: Asia has better numbers

## Slide 10: And similar diversity

## Slide 11: DNSSEC adoption

## Slide 12: Europe is (slightly) ahead

## Slide 13: Same (but different) diversity
DNSSEC is deployed in Northern Europe,
but not as much in Central, Southern or
Eastern Europe

## Slide 14: Asia has been steady for 24 months

## Slide 15: And again a diverse spread

## Slide 16: RPKI ROV Adoption
All End Users behind ROV-aware filters: 14%
European users: 10%
Asian users: 10%

## Slide 17: RPKI ROV Adoption in Europe
Rate of RoV Filtering

## Slide 18: RPKI ROV Adoption in Asia
Rate of RoV Filtering

## Slide 19: Why is there such diversity in deployment?

## Slide 20
Challenges for adoption:
This is a deregulated and
competitive environment
There are many different players
Each with their own perspective
?
And all potential approaches will be explored!

## Slide 21
Challenges for adoption:
2. The myth of long-term planning
?
“IPv6 Transition will take many years...
5 years, maybe 10 years, maybe longer”
Are we still firmly committed to the plans we had 5 years ago? How about our 10-year-old plans?
The longer the period of transition, the higher the risk of completely losing the plot and heading into other directions!

## Slide 22: Today’s Internet Architecture
Challenges:
The Internet keeps changing

## Slide 23: Some providers see advantage in adoption
Competitive positioning in a diverse market
Early adoption of future mainstream technologies (first user advantage)
Perception of enhanced utility, security and safety in these more recent technologies

## Slide 24: Others see reasons to wait …
IPv6 is a 1990’s technology solution to a 1980’s networking architectural challenge – CDN feeder networks do not need globally unique address plans across every device all of the time
DNSSEC is only partially-implemented. If we pushed DNSSEC validation to the edges of the network we’re scared that the DNS will slow down to unacceptable levels.
RPKI Route Origin Validation makes DNS route hijacking only slightly harder. More moving parts can introduce fragility, and not necessarily enhance operating stability

## Slide 25: Lets return to Bhutan
And see which service providers have adopted each of these technologies

## Slide 26: Bhutan and DNSSEC

## Slide 27: Bhutan ISPs and DNSSEC

## Slide 28: Bhutan and DNS Resolver Use
ISP Resolver
Google
Different AS, still in Bhutan
Cloudflare

## Slide 29: Bhutan and DNS Resolver Use
ISP Resolver
Google
Different AS, still in Bhutan
Cloudflare
This is TashiCell Mobile (AS134417) using DNS resolvers in Tashicell Domestic AS 23955)

## Slide 30: Bhutan and DNS Resolvers
Chinese open resolvers
Other resolvers not in Bhutan
ISP Resolver
Other resolvers in Bhutan

## Slide 31: Bhutan and ROV Filtering

## Slide 32: Bhutan and ROV Filtering
Obviously AS18024 (Bhutan Telecom) is not ROV filtering yet
This is impressive!

## Slide 33: Bhutan and ROA Production IPv4

## Slide 34: Bhutan and ROA Production IPv6

## Slide 35: And then there’s IPv6

## Slide 36: And then there’s IPv6

## Slide 37: And then there’s IPv6
WHY so low?

## Slide 38
Thanks!