## Slide 1: Measurement of DNSSEC Validation with RSA-4096
Geoff Huston, Joao Damas
APNIC Labs
November 2021

## Slide 2: RSA is not a “dense” algorithm
Security “level” (bits) * | RSA Key Length (bits)
80 | 1,024
112 | 2,048
128 | 3,072
140 | 4,096
192 | 7,680
* An n-bit security level implies that an attacker would need to perform 2n operations to “solve” it.

## Slide 3: And quantum computing is an “issue”
(using a mere 20 million qubit quantum computer!)

## Slide 4: What if…
You’re concerned by this because:
  You want to protect the data for longer than 8 hours
  You believe that quantum computers will develop quickly
  You believe that ECDSA represents a lower level of resistance to quantum computing techniques
So you might want to keep using RSA, but extend its key length to defend against this risk
To 4,096 bit keys perhaps?

## Slide 5: Will RSA-4096 work for DNSSEC?
The major concern is the size of the data to be carried in DNS payloads
Algorithm | Private Key (bytes) | Public Key (bytes) | Signature (bytes) | Security Level
RSA-1024 | 1,102 | 438 | 259 | 80
RSA-2048 | 1,776 | 620 | 403 | 112
RSA-4096 | 3,312 | 967 | 744 | 140
ECDSA P-256 | 187 | 353 | 146 | 128
Ed25519 | 179 | 300 | 146 | 128
These sizes impact DNS payload sizes

## Slide 6: RSA-4096 Performance
Signing Time is the elapsed time to size a zone with 0.5M entries
Validation Time is the elapsed time to validate 50K responses
Algorithm | Signing Time (secs) | Validation Time (secs)
None |  | 905
RSA-1024 | 52 | 1,168
RSA-2048 | 126 | 1,173
RSA-4096 | 830 | 1,176
ECDSA P-256 | 159 | 1,036
Ed25519 | 205 | 1,008

## Slide 7: RSA-4096 signed DNS Response sizes by Query Type
RR Type | RSA-4096 (bytes) | ECDSA P-256 (bytes)
A | 747 | 273
DS | 721 | 245
DNSKEY | 1,245 | 347
DNS Flag Day 2020 proposed a maximum DNS payload of
1,232 bytes when using UDP transport

## Slide 8: Will it fit?
If we are looking at the point of UDP truncation then we need to look at the distribution of EDNS(0) UDP Buffer size settings on these DNSSEC validation queries
17% of users query via recursive resolvers that use a UDP buffer size of less than 1,245 bytes

## Slide 9: Test Rig
Configure an Ad campaign to ask for 2 URLs:
  One has a domain name that is signed using an RSA-4096 key
  One uses an invalidly signed domain name, again using a RSA-4096 key
The Domain names are dynamically generated with unique sub-labels
We perform a DNS packet capture at the authoritative server
We are looking for experiments that use resolvers that ask for DS and DNSKEY records
https://0ds-udeb9087f-c13-a1283-s1632968189-i00000000.ape.dotnxdomain.net/1x1.png
https://0di-udeb9087f-c13-a1283-s1632968189-i00000000.ape.dotnxdomain.net/1x1.png

## Slide 10: Experiment result classes
“Validating”
  The A / AAAA queries have the DO bit set
  DS / DNSKEY queries are made
  The user fetches the validly signed web object, but not the invalidly signed object
“Mixed Validating”
  The A / AAAA queries have the DO bit set
  DS / DNSKEY queries are made, but not necessarily by every resolver
  The user fetches both the validly-signed and invalidly signed web objects

## Slide 11: Single RSA-4096 Key
The zone uses a single yet as both the KSK and the ZSK
The DNSKEY records contains a single key
Test of 84M samples over 7 day period in September 2021
Algorithm | Validating (% of tests) | Mixed (% of tests)
RSA-1024 | 29.7% | 9.0%
RSA-4096 | 29.4% | 9.1%
We use a RSA-1024 signed zone as a control, where the DNSKEY response is 491 octets

## Slide 12: RSA-4096 DNSKEY response processing
74% of experiments received the DNSKEY response of 1,245 bytes over UDP
26% of experiments had a smaller UDP buffer size and were sent a truncated UDP response
  23.5% of experiments followed up using TCP
  And 2.5% did not!
    2% then re-queried with a different resolver that used a larger UDP buffer size
    0.5% failed DNS resolution

## Slide 13: But maybe this is not a “real” test
Perhaps a more realistic scenario for a DNSSEC-signed zone is to use a ZSK and a separate KSK, which means we should look at the DNSKEY record with 2 x RSA-4096 keys
And we should also consider a key roll scenario, which means we should also look at the DNSKEY record with 3 x RSA-4096 keys
So let’s go there!

## Slide 14: Multiple RSA-4096 Keys
Key Count | DNSKEY Response Size (bytes)
1 x RSA-4096 | 1,245
2 x RSA-4096 | 1,755
3 x RSA-4096 | 2,237

## Slide 15: Validation Outcomes with larger DNSKEY records
Algorithm / Key Count | Validating | Mixed
RSA-1024 | 29.7% | 9.0%
RSA-4096 x 1 | 29.4% | 9.1%
RSA-4096 x 2 | 27.9% | 9.1%
RSA-4096 x 3 | 24.0% | 7.8%
The comparison between the 2-key and 3-key cases shows that there are more issues than just UDP fragmentation and/or TCP re-query when the DNS response grows from 1,755 to 2,237 bytes
Are we touching upon internal implementation issues? Or perhaps selective network responses to pre-empt potential DNS amplification attacks? Perhaps other causes are at work here to create this difference between the outcomes of these two cases.

## Slide 16: What’s going on?
Maybe the resolver’s UDP Buffer size in queries is being too optimistic and doesn’t reflect the resolver’s ability and the local network’s ability to admit fragmented UDP responses and reassemble the responses
  Path MTU mismatch, security policies, receiver buffer limits?
Or
The resolver is unable to perform a TCP fetch after receiving a truncated UDP response
  Over-enthusiastic local security rules, or borked DNS implementations, misbehaving middleware, or load-distribution front end size filters?

## Slide 17: Failure to complete a TCP re-query rises with a larger DNS PAYLOAD
Key Count | TCP Failure Rate
RSA-4096 x 1 (1,245 bytes) | 0.1%
RSA-4096 x 2 (1,755 bytes) | 2.5%
RSA-4096 x 3 (2,237 bytes) | 7.2%
Here we are looking for a query sequence where we respond to the original query with a truncated UDP DNS response, but there is no subsequent TCP completed re-query

## Slide 18: Where is this a problem?
 | RSA-1024 | RSA-4096x2 | Difference
Portugal | 68% | 40% | -28%
Morocco | 59% | 31% | -27%
Iceland | 95% | 72% | -23%
Guyana | 41% | 28% | -13%
USA | 60% | 48% | -12%
Ireland | 27% | 18% | -9%
Switzerland | 81% | 73% | -9%
Brunei | 31% | 23% | -8%
Singapore | 71% | 64% | -8%
Sweden | 91% | 84% | -7%
These are all % of users who complete DNSSEC Validation

## Slide 19: Which ISPs?

## Slide 20: Does RSA-4096 have a future in DNSSEC?
It’s not looking good!
But does it matter?
Should we be turning to using 140-bit security level in DNSSEC in 2021 in any case?
  (i.e. is RSA-4096 over-achieving for DNSSEC?)

## Slide 21: It’s DNSSEC!
What is the “secure lifetime” of a signed item of DNS data?
  It’s not hiding a “secret”!
  It‘s protecting the integrity of the DNS data
  And the integrity of the digital signature depends on the key lifetime
  So the anticipated secure lifetime of a DNSSEC key needs to be greater than the key lifetime, but not that much longer!
So the longer the lifetime of a DNSSEC key, then the greater your requirement for a longer secure lifetime, which implies the greater your need a higher security level of your algorithm and key
  For example, if your roll keys every 6 months then your secure lifetime requirement is less than 1 year
While RSA-1024 is probably incapable of providing a 10 year secure lifetime for encrypted messages, it is likely to still be useful in DNSSEC as long as you roll your keys more frequently than every decade!

## Slide 22: It’s Quantum Computing!
In our current understanding of the quantum computing environment the concept of “security level” does not transcribe from conventional to quantum computing cleanly
While some algorithms and key profiles have the same “security level” they have different levels of quantum resilience
For example, RSA with longer keys lengths is thought to be more quantum resilient than an equivalent security level elliptical curve profile

## Slide 23: Questions?